SECTION 602	-	EXCAVATIONS

##This section cross-references Section 614.

If Section 614 is relevant, it should be included in the specification.

If Section 614 is not included in the specification, all references to it should be struck out, ensuring that the remaining text is still coherent:

602.01	GENERAL

Excavation shall consist of all clearing and grubbing necessary to clear the way for proposed excavations, the excavation of  foundation pits or interiors of cofferdams or cylinders, the preparation of foundation, and shall include all sheeting and bracing, drainage, pumping or bailing, and other necessary work and materials.

602.02	TIMBERING AND SUPPORT

For excavations in soil or in rock containing unfavourable jointing, bedding or weak seams, which are deeper than 1.5 m the Contractor shall provide adequate support or benching to prevent collapse of excavation faces and/or heaving of excavation base.  Works shall be undertaken in accordance with all relevant Acts, Regulations and Codes and in particular the Work Health and Safety Act 2012.

For excavations adjacent to railway property, alongside roadways, in or alongside waterways, and excavations deeper than 1.5 m, the Contractor shall submit to the Superintendent for review detailed drawings of bracing and/or sheeting proposals, including design calculations and methods of construction and removal, not less than 10 business days prior to excavation commencing.

For excavations carried out adjacent to railway property, obtaining approval of the appropriate railway authority and rail entities shall be the responsibility of the Contractor.

HP	No excavation adjacent to railway property shall commence without the approval 	of the Superintendent.

All works and the quality of all materials used for the temporary support of excavations shall conform with the appropriate Australian Standards.

602.03	EXCAVATION PREPARATION

Water shall not be permitted to remain in the bottom of excavations during construction.

The quality of the material (rock or soil) exposed in the side walls and at the bottom of the excavation shall be inspected by a geotechnical consultant with suitable experience to confirm that the material is of the type and quality indicated on the drawings. All loose material and pockets of unsound material, mud and/or water shall be removed to expose the foundation material being of the type and quality indicated on the drawings.

The bottoms of excavations shall be trimmed in horizontal beds or steps.  The steps shall have maximum vertical rise height to horizontal run length of 1 to 5 ratio.

Where the excavation is for construction of footings, the sides of footings shall be formed in accordance with Section 614 - Formwork.  The Contractor may dispense with formwork for the sides of the footing if all unsupported faces of the excavation are inspected by a geotechnical consultant, who confirms the material exposed in the unsupported faces has the material strength to maintain the stability of the faces without external (e.g. formwork) or internal support (e.g. soil nailing).

Where concrete is cast against an unformed surface, an extra 25 mm cover shall be provided to the reinforcement.

The bottom of any excavation which has been disturbed by the action of water or any construction activity such that it does not meet the specification requirement shall be rectified by the Contractor.

HP	Blinding, sealing or foundation concrete shall not be placed until the bottom of the 	excavation has been reviewed by the Superintendent.

Within 24 hours of a request from the Superintendent, the geotechnical inspection reports shall be submitted to the Superintendent for review.

The Contractor shall provide appropriate facilities for the inspection of all work and shall be responsible for all costs associated with the provision of such facilities and the engagement of a geotechnical consultant who shall be pre-qualified with VicRoads or approved by the Superintendent.

# Text boxes

Department of State Growth – August 2016

Section 602 (Page 2 of 2)

Department of State Growth – August 2016

Section 602 (Page 1 of 2)