SECTION 670	-	STEEL BRIDGE BARRIERS

##This section cross-references Sections 175, 610, 630, 631 and 675.

If any of the above sections are relevant, they should be included in the specification.

If any of the above sections are not included in the specification, all references to those sections should be struck out, ensuring that the remaining text is still coherent:

670.01	GENERAL

This section covers the fabrication and installation of steel barriers for road and pedestrian bridges.

Section 175 details the relevant references to Australian Standards (AS) in this section.

670.02	MATERIALS AND FABRICATION

Materials and fabrication of steel components shall be in accordance with Section 630.

Materials and fabrication of cast steel posts and sleeves shall be in accordance with Section 675.

Where the drawing requires the steel barrier posts to be cut before welding to the structure, the Contractor shall make an allowance (not exceeding 20 mm) for packing or cutting the posts to allow for variation of camber.

670.03	INSTALLATION OF BARRIERS

The barrier shall be installed in accordance with Section 630 and to the tolerances specified in Clause 670.05, to a smooth alignment both vertically and horizontally independent of any irregularities that may exist in the alignment of the deck.

Barrier posts, panels, balusters and openings shall be vertical.

Bolts, nuts, washers, base plates and welds shall be of the correct sizes and shall be correctly assembled.

Retrofitted bonded anchors shall not be used in anchor-bolts for steel barriers.

Sleeves at expansion joints shall be connected to the rail on the lower side of the joint.

Bolted joints at sleeves joints and rail splices shall be as shown on the drawings and as specified. Hole drilling shall be in accordance with Section 630 and any cut surfaces (holes) shall have a protective coating treatment applied in accordance with Section 631.

After the barrier has been installed and all connections made, the gap between the base plate and the top of concrete footing shall be completely filled with a flowable dual shrinkage compensating proprietary cementitious grout in accordance with Clause 610.32.  Dry pack mortar shall not be used.

HP	Railing posts shall not be grouted until the Contractor provides a Survey Certificate verifying compliance with the specified tolerances on lines and levels.

670.04	BARRIER FINISH

The type and extent of the primary protective coating and additional paint finish shall be as shown on the contract drawings and as specified.

The finished surface of barriers shall be smooth, non-abrasive and non-snagging.

Both internal and external surfaces of barrier railing and posts shall have a hot-dip galvanized (zinc) coating applied in accordance with AS/NZS 4680.

Where the barrier is completely sealed by welding against the ingress of water and other corrosive agents, a zinc silicate primer may be applied for external protection in lieu of galvanising.  The primer shall be applied in accordance with Section 631.

Where required, additional paint finishes for secondary protective coatings or aesthetic and other reasons shall be applied in accordance with Section 631.

670.05	TOLERANCES

Barriers shall be installed within the following tolerances:

(a)	Departure from plan position 	 25 mm

(b)	Departure from alignment 	 5 mm

(c)	Irregularities in alignment 	 3 mm in 3 m

(d)	Variation in joint gap width 	 3 mm

(e)	Verticality of posts, panels, balusters and openings 	 ( 2 mm.

# Text boxes

Department of State Growth – August 2016

Section 670 (Page 1 of 2)

Department of State Growth – August 2016

Section 670 (Page 2 of 2)